# SAFE OPERATING PROCEDURE

Brush Cutter Petrol Operated

DO NOT use this machine unless you have received instruction and training in its safe use and operation.

| Safe Work Procedure Checklist: |
| --- |
| PRE-OPERATIONAL SAFETY CHECKS Check unit for loose/missing nuts/parts. Inspect fuel lines and tank for leaks. Ensure that all guards are fitted and secure. Ensure the harness is attached. Ensure cutting tool is fitted correctly. Check blades for damage and cracks. If using the nylon line cutting head ensure line is correct dimensions. Faulty equipment must not be used. Report suspect machinery immediately. OPERATIONAL SAFETY CHECKS Adjust the handle/s to a position for comfort and good balance. When starting, ensure the line or blade cannot contact the ground or any other obstruction. The muffler side of the engine should be away from your body to avoid burns. Maintain footing and balance at all times. Do not work on slippery, uneven or unstable surfaces. Maintain a straight wrist position Avoid using your wrist in a bent, extended or twisted position for extended periods. Always keep both hands on the control handles. Do not operate one-handed. Do not raise the line or blade head above knee height. Keep machine clear of fences, wires, posts, rocks, etc. to prevent kick out and cutter head damage. Shut down immediately if the unit starts to shake or vibrate. After shutting down the engine, keep fingers and feet away from the cutting line or blade until all rotation stops. Disconnect spark plug wire before you work on the unit or leave it unattended. Take extreme caution when refuelling to avoid igniting fuel on hot exhaust or engine. HOUSEKEEPING Remove any foreign material from engine, cutting tool and guards. Keep the work area and implement shed in a clean and tidy condition. Keep any person or animal a minimum 15 metre radius away from the working area. |
| POTENTIAL HAZARDS ( Entanglement ( Impact ( Cutting ( Shearing ( Crushing injuries ( Electrical ( Fire/explosion ( Ergonomics, ( Vibration, ( Noise, ( Slips, trips and falls ( Dust, ( The blade can push, pull or kick out. |
| Date of Review: | Signature |